## Slide 1
A High-Resolution 3D Hypoxia Model (GEM3D)
for the Louisiana Shelf
Dong S. Ko1, John C. Lehrter2, Michael C. Murrell2, Richard M. Greene2, Richard W. Gould1, and Bradley Penta1
1 Naval Research Laboratory, Stennis Space Center, MS 39529
2 U.S. EPA, 1 Sabine Island Drive, Gulf Breeze, FL 32561
Louisiana
Forum for Gulf of Mexico Hypoxia Research Coordination and Advancement
17-18 April 2013, Stennis Space Center, Mississippi
Notes: Support comes from EPA

## Slide 2
EPA General Environment Model (GEM)
Peter M. Eldridge and Daniel L. Roelke (2010, Ecological Modeling)
Consists of a plankton food web model that has 6 phytoplankton groups
and 1 zooplankton group
A multi-element diagenetic model that traces oxygen, nitrogen, phosphate,
carbon and various organic matters with exchange of O2 and CO2 at surface
Notes: GEM3D is an integration of EPA GEM and 3D high-resolution coastal circulation model IASNFS-LCS

## Slide 3
Ko, D.S., R.H. Preller, and P.J. Martin, 2003: An Experimental Real-Time Intra Americas Sea Ocean Nowcast/Forecast
System for Coastal Prediction, Proceedings, AMS 5th Conference on Coastal Atmospheric & Oceanic Prediction &
Processes, 97-100.
Ko, D.S., P.J. Martin, C.D. Rowley, and R.H. Preller, 2008: A real-time coastal ocean prediction experiment for MREA04,
J. Marine Systems, 69, 17-28, doi:10.1016/j.jmarsys.2007.02.022.
Lehrter J.C. , D.S. Ko, M.C. Murrell, R.M. Greene, J.D. Hagy, B.A. Schaeffer, R.W. Gould, B. Penta, 2013: Nutrient
transports and source/sink dynamics on the inner Louisiana continental shelf, J. Geophy. Res., submitted.
IASNFS-LCS Circulation Model
A fine resolution (~2 km/34 layers) fully 3D circulation model based on NCOM
Nested in the Intra-Americas Sea Nowcast/Forecast System (IASNFS)
95 Rivers with real-time runoff
Notes: IASNFS-LCS cover Louisiana Continental Shell and is nested in large scale IASNFS

## Slide 4
Intra-Americas Sea Nowcast/Forecast System (IASNFS)
From 2003 up-to-date
http://www7320.nrlssc.mil/IASNFS_WWW
Longitude : 98 W – 55 W; Latitude : 5 N – 31 N
Horizontal Resolution : 1/24 Degree (~ 6 km)
Vertical Resolution : 40 Layers (19 Layers on the shelf)
140 Rivers with real-time river discharge
Notes: IASNFS provides IASNFS-LCS with boundary conditions. IASNFS is in real-time operation at NRL since 2003.

## Slide 5
Predicted particle distributions for 20 May initialized from 17 May satellite analysis (shown in gray) using surface currents from (a) NOAA NGOM model, (b) NRL IASNFS model, (c) NAVO Global NCOM model, and (d) TGLO model.
Notes: During 2010 oil spill, IASNFS provides daily forecast to NOAA for oil trajectory prediction.

## Slide 6
IASNFS Current over Altimeter SSH
IASNFS Current (5-day average) is consistent with Altimetry
Notes: IASNFS current is consistent with altimeter ssh, predicting Loop Current/Loop Current eddies.

## Slide 7
IASNFS SSHa vs Altimetry Analysis
In deep water > 500m
Overall very good correlation except during the period when altimetry analysis has large errors
Altimetry analysis
relative error
Blue: small error
Dark red: large error
Notes: Good correlation with altimeter ssh Cr = .87

## Slide 8
IASNFS Currents vs Mooring Observation
Notes: Good comparison of current with BOEM mooring measurements

## Slide 9
IASNFS SSH Variation vs NOS Tide Gauge
Overall very good correlation
Altimetry analysis
relative error
Notes: Very good correlation with NOS tide gauge sea level variation

## Slide 10
IASNFS SSH Variation vs NOS Tide Gauge
Monthly
Notes: Good correlation with tide gauge in seasonal scale

## Slide 11
IASNFS SST vs NDBC Buoy
Very good correlation
Altimetry analysis
relative error
Notes: Very good comparison with NDBC buoy sst in the Gulf of Mexico

## Slide 12
IASNFS SST vs MCSST
Very good correlation
Altimetry analysis
relative error
Notes: Very good comparison with MCSST

## Slide 13
IASNFS-LCS Simulation
From 2002 to 2012
Surface Salinity
http://www7320.nrlssc.navy.mil/IASNFS_WWW/EPANFS_WWW/
Notes: IASNFS-LCS simulation

## Slide 14
IASNFS-LCS Tides vs NOS Tide Gauge
Notes: Good correlation in tides

## Slide 15
IASNFS-LCS Tides vs NOS Tide Gauge
Notes: Good correlation in sub-tidal wind-driven sea level variation

## Slide 16
IASNFS-LCS SST vs NDBC Bouy
Notes: Very good correlation with NDBC sst measurement

## Slide 17
IASNFS-LCS SST vs MCSST
Notes: Very good correlation with MCSST (short-time variation is reduced)

## Slide 18
IASNFS-LCS Simulation with Kd
Kd from
SeaWiFS/MODIS
Without Kd
Temperature
With Kd
Temperature
Notes: Use Kd from SeaWiFS/MODIS to improve temperature prediction

## Slide 19
IASNFS-LCS Simulation with E-P
Precipitation from TRMM
Evaporation from COAMPS
RMSE = 1.4
RMSE = 0.7
1:1
1:1
Notes: Use rainfall from TRMM to improve salinity prediction

## Slide 20
IASNFS-LCS Simulation with E-P
Without E-P
Salinity
With E-P
Salinity
Notes: Difference in salinity prediction with/without TRMM rainfall

## Slide 21
IASNFS-LCS Simulation with E-P/Kd
RMSE =1.09
RMSE = 0.55
1:1
1:1
RMSE = 1.4
RMSE = 0.7
1:1
1:1
Without E-P/Kd
With E-P/Kd
Notes: The salinity prediction improve somehow with TRMM

## Slide 22
IANFS-LCS Simulation - Flow Pattern
Monthly Mean Current (vectors) & EKE (colors)
Notes: Overall IASNFS-LCS simulation shows correct seasonal flow pattern

## Slide 23
IASNFS-LCS Simulation - Stratification
Seasonal Stratification On the Louisiana Shelf
(Brunt-Vaisala / Buoyancy Frequency)
Notes: And seasonal stratification

## Slide 24
GEM3D Simulation – Riverine OM
Horizontal Variation due to River Runoff, Settling,
3D Current Advection and Vertical Mixing
Notes: All 30 variables in the GEM3D are subjected to 3D advection (with sinking) and vertical mixing over more than 1 million grids every time step (300s).

## Slide 25
Day-Night Variation
Zooplankton
GEM3D Simulation of Plankton Dynamics
Vertical Variation is also due to Migration, Growth, Death and
3D Advection by the Current
Light
Depth
Phytoplankton
Zooplankton
Notes: With high vertical resolution, an improved plankton dynamics

## Slide 26
GEM3D Simulation - Phytoplankton
Total (Monthly Average)
Initialized with NOAA NODC monthly DIN, DIP and DO climatology
The monthly climatology is also used for the open boundary conditions
Real-time daily river runoff from USACOE/USGS

## Slide 27
GEM3D Simulation - Phytoplankton
Total 6 Groups

## Slide 28
GEM3D Simulation - DIN

## Slide 29
GEM3D Simulation - OM at Bottom
Daily

## Slide 30
GEM3D Simulation – OM
3 Groups

## Slide 31
GEM3D Simulation - Bottom Water DO
Daily

## Slide 32
GEM3D Simulation - Bottom Water DO
Monthly Average

## Slide 33
GEM3D Simulation - DO

## Slide 34
km2
Observation
Comparison of Observation to the model predicted area of bottom water hypoxia that is persistent over 10 days or over 15 days for the season.
The observed area of bottom water hypoxia is an estimation based on ship surveys. The estimation for 2011 is 17,548 km2 (LUMCON). For 2012 is 7,480 km2 (Jul 27).
For 2010, the hypoxic zone is in part located at Texas shelf out of model domain.
EPA-GEM3D Simulation - Area of Bottom Water Hypoxia
Each Season from 2003 to 2012